## Slide 1: OreSat Command, Control and Communications Module AKA: Sputnik
Members:
William Harrington
James (Jake) Heath
Michael Mathis
Shan Quinney

## Slide 2: Introduction
PSAS/OreSat’s mission is to get a CubeSat into Lower Earth Orbit
Need for a device for command, control and communication (C3) between a CubeSat and a ground station
The code name for the module is Sputnik because of it's requirements to be a simple, reliable space system.
Notes: Problem or Need : What is the problem being solved? Where does it arise?
 Portland State Aerospace Society has a need of a device that can communication between a CubeSat and a ground Station. The commercial Boards
2

## Slide 3: Motivation
Launch Oregon’s first small educational satellite (aka CubeSat)
Build the first and most important avionics modules for the CubeSat
NASA ELANA program

## Slide 4: Objective
Rapidly prototype C3 Module that can
  Handle long distance RF communications to and from a Low Earth Orbit
  Controlling and communicating with a payload that is housed within the CubeSat
Notes: What is the specific objective of this project?A design? Aworking prototype?
4

## Slide 5: Bigger Picture
Building a C3 system from scratch to meet
  The harsh environment of space
  Compliance with governmental regulations
Programming the module to perform the aforementioned duties
Testing and verifying the device
Documentation
Adhering to the PSAS open-source standard

## Slide 6: Requirements
Must
  Environment
    Use parts rated in an Industrial Operating Temperature Range (−40°C to 80°C)
  Communication block ("radio")
    Operate in the 70 cm band (436 to 438 MHz)
      Use IARU specified frequency for RF comms and make appropriate changes if necessary
    Meet FCC Amateur Radio Licensing requirements (Title 47 CFR part 97)
    Meet 10km link budget
    Have bidirectional communication interface to Payload via UART
    Local storage for communication in/out queues
  Energy storage
    Use an energy storage system to power the modules when not in sunlight
  Energy Switching/Control
    Be able to seamlessly switch energy sources to the load (System Controller)
  System controller ("Controller")
    Radiation tolerant analogue "system watchdog" controller
    Power switches to turn other blocks on and off
    Monitor energy storage and energy harvesting systems (no)
    Communication link with communication block (kind of)
  CubeSat requirements
    Conforms to latest CubeSat specification where applicable
    Fits in 1/4 1U CubeSat
    Weighs less than 250 g

## Slide 7: Stretch Goals
Should
  In general
    Use as many COTS (Commercial Off The Shelf) parts as possible
  Energy Storage
    Monitor the state of charge of the battery
      Voltage
      Current
      Charge (Coulombs)
  Environment
    Operate in the Automotive Operating Temperature Range (−40°C to 125°C)
    Be able to operate in a near-perfect vacuum
    Handle 15g in the "Z" axis
  Communication block (“radio”)
    Use a frequency of 436.5 MHz for RF communication
May
  Environment
    Operate in Military Operating Temperature Range (-55°C to 125°C)

## Slide 8: Approach
Decided to have two separate modules that together make C3
  LGR – Low Gain Radio
    Communications pipeline
  System controller
    Receive and execute commands (Command/Control)
Divide and conquer!
  LGR – Will, Jake
  System Controller – Shan, Mike

## Slide 9: OreSat Low Level Diagram
Notes: May need multiple subAheadings here (e.g. H/W and S/W, or multiple subsystems) Describe design using appropriate methods (e.g. UML models, algorithms) Discuss design alternatives, tradeAoffs, decisions made
9

## Slide 10: Sputnik Low Level Diagram
Notes: May need multiple subAheadings here (e.g. H/W and S/W, or multiple subsystems) Describe design using appropriate methods (e.g. UML models, algorithms) Discuss design alternatives, tradeAoffs, decisions made
10

## Slide 11: Low Gain Radio (LGR)
Definition
Purpose
Requirements
Block Diagram
Schematic
Layout
Firmware
Testing Results

## Slide 12: LGR - Definition
Low-gain radios (LGRs) provide wide-angle coverage, but in turn have lower gain. LGRs are designed to be useable for relatively low data rates as long as the satellite is within line of sight of the receiver.
Low-gain so that we can control the CubeSat no matter what the orientation
Main communication pipeline for the satellite

## Slide 13: LGR – Requirements
Operate in the 70 cm ISM band
  436.5 MHz
Meet 400 km link budget
  Need output power of up to 1 Watt
Adhere to FCC Amateur Radio Licensing requirements (Title 47 CFR part 97)
  2nd Harmonic is less than 40dB of desired signal strength
Have bidirectional communication interface to system controller via UART
Local storage for communication in/out queues

## Slide 14: LGR - Block Diagram

## Slide 15: Implementation - LGR Schematic
Notes: 15

## Slide 16: Schematic - Filter

## Slide 17: Implementation – PA Schematic

## Slide 18: Implementation – LNA Schematic

## Slide 19: Schematic – RX/TX Switch

## Slide 20: Schematic – MCU

## Slide 21: Schematic – SPI Cache/MCU LDO

## Slide 22: Schematic – Debug Pins

## Slide 23: Board Layout (LGR)
Notes: 23

## Slide 24: Layout - MCU/SPI Cache

## Slide 25: Layout - RF

## Slide 26: LGR Firmware
Drivers
  Clock
  GPIO
  SPI
  UART
  Transceiver
Main loop
  RX/TX
    Uses SPI
  Print to UART
  Blink LEDs

## Slide 27: LGR Testing
Main Tests:
  Supply Range Test
    Ensure radio works over variable range from 3-5 V
  Filter Tests
    Practicum filters
  Radio Test
    Confirms radio is capable of transmitting and receiving
  Functionality Test
    Confirms radio transmission distance

## Slide 28: LGR – Supply Range Test

## Slide 29: Filter Measurements

## Slide 30: LGR - Radio Test

## Slide 31: System Controller (SC)
Definition
Purpose
Main contributors
Requirements
Block Diagram
Schematic
Layout
Firmware
Testing Results

## Slide 32: Purpose
The System Controller is entrusted to perform two main tasks that are essential to the success of the CubeSat. These include the task of system monitor (watchdog) and the task of power management.
The System Controller is the second of the two boards completed for the Sputnik C3 Capstone. It contains an ATMega128 microcontroller, optical isolation between itself and the LGR and FC boards, and the power management circuitry for the system.

## Slide 33: Block Diagram

## Slide 34: Implementation – SC Schematic
Notes: 34

## Slide 35: Implementation – Optoisolator Schematic

## Slide 36: Implementation – eFuse Schematic

## Slide 37: Board Layout (SC)
Notes: 37

## Slide 38: System Controller Firmware
ATMega microcontrollers have a very developed driver ecosystem
The system controller listens on UART and I2C for status updates from the payload, LGR, and power system
If there is an error with module, possibly due to a radiation latch-up event, the system controller can power cycle each subsystem individually
  If the power system needs to be reset, the system controller is powered by the on-board super capacitor. This can power the system controller for 15-30 seconds
When the system controller listens to the LGR it will also recognize commands sent from the ground station and execute them

## Slide 39: SC Testing
Add SC testing video

## Slide 40: Sputnik Functionality/Distance Test
Notes: Example of System Testing
40

## Slide 41: Distance
OHSU
Rocky
Butte
Total Distance:
10.57 km
Notes: Example of Interface Testing
41

## Slide 42: Test Setup
Pictures of testing and video
Notes: Example of Interface Testing
42

## Slide 43: Sputnik Test Results
Test | Result
Component Test | Passed
Supply Range Test | Passed
Radio Test | Passed
Command Test | Passed
Control Test | Passed
Final Test | Passed

## Slide 44: Requirements with Results
Initial Requirements | Final Status | Completion
Parts temperature rated (-40 to 80C) | No change | Completed
Radio in 70cm band | No change | Completed
10km link budget | No change | Completed
Power without sunlight | No change | Completed
Energy source switching | No change | Completed
Environmental Tests (vacuum, temperature, acceleration) | Removed | N/A – The prototype will not be used in harsh environments
Radiation Tolerant Watchdog | No change | Completed
Power switches for other blocks | No change | Completed
Conforms to CubeSat standard | No change | Completed
Monitor Energy Storage | Removed | N/A - Power system management removed

## Slide 45: Budget Up to $1000
Item | Cost
System Controller Stencil (2) | $33.46
Low-Gain-Radio Stencil (2) | $52.08
System Controller Parts (With Spares) | $307.96
Low Gain Radio Parts (With Spares) | $200.89
System Controller Board (3) | $153.70
Low Gain Radio Board (3) | $153.70
Total | $901.79

## Slide 46: Impact
Open Source low-budget CubeSat project that can be used by smaller developing aerospace groups as a jump off point.
  Also will be the first legible open source code for setting up the MCU on the LGR.
First CubeSat from Oregon to be apart of the NASA ELANA program.
Another step in a new direction of interest for PSAS.

## Slide 47: Changes and Improvements
Get rid of Freescale/NXP MCU (maybe?). Texas Instruments has a good alternative that was vaporware at the beginning of the project.
Change the RF Switch to suit our layout needs better and get rid of the inverter.
Change MACOM LNA chip to a new Skyworks LNA that has better data within our frequency range.

## Slide 48: Lessons Learned
Earlier hack sessions, saved too many difficult tasks for too late in the term
More communication between teams, particularly between hardware and firmware
Work on harder tasks together

## Slide 49: IP and Prior Work
Datasheets
Freescale/NXP
Silicon Labs
Murata
Microchip Technology
Micrel
All open source
ATMega drivers from Peter Fleury
Notes: Brief summarize what use you made of prior work or IP including but not limited to ideas, designs, schematics, board layouts, code.
49

## Slide 50: Acknowledgments
Portland State University
Aerospace Society (PSAS)
  Andrew
  Glenn
  Theo
  Kenny
  Jaime
  Eric
Notes: 50

## Slide 51: Q&A / DEMO