## Slide 1
As of 5/24/2016 the accomplishments of the project include:
Finished Low-Gain Radio board
  Current limited power tests have worked
  Carrier signal at desired power and frequency has been transmitted
  Working on packet transmissions
Finished System Controller design
  Waiting for board delivery to commence building
  Firmware complete on evaluation board.
Department of Electrical and Computer Engineering
Project Team:
Will Harrington
Jake Heath
Michael Mathis
Shan Quinney
Special Thanks to:
Andrew Greenberg Theo Hill
Glenn Dr. Teuscher
PSAS The LID
Pictures of the finished boards LGR (left) and SysCon (right)
Introduction
Design
Current Results
CubeSat Command Control
and Communications System
The Portland State Aerospace Society (PSAS) is the lead on the Oregon Small Satellite Project. “OreSat” is a CubeSat form-factor nanosatellite designed for a low-earth orbit of 400 km.
OreSat requires a robust command, control, and communication (C3) system to control the satellite. The C3 system must communicate to the ground over 1,400 km (at acquisition of signal) at low data rates (9600 bps) while monitoring and controlling the power system of the satellite.
Completed boards for the LGR (left) and the SC (right)
Carrier Signal (Left) and the 10km test location (Right)
Jake Heath working on an LGR module
Our design is only two of the many modules in OreSat. The LGR is used for communication with the Cubesat, supplying 1 Watt of transmission power to cover the long distance. The System Controller, which will be accessible from the ground station via the LGR, will inform the ground crew in the case of radiation latch-up and can restart the whole satellite if necessary.
We split our design into two parts, the Low-Gain Radio (LGR) which handles communication and the System Controller (SC) which is in charge of command and control for the module
The boards need to be cut in order to fit properly.
The layout of the LGR (left) and the SC (right)
Little Beacon Rock
Vista House